## Slide 2
Introduction
Ultrasonic Principles
Test Equipment
Test Preparation
Data Acquisition
Documentation

## Slide 3
Introduction
    To apply the proper testing technique
    Interpret, evaluate and make a skillful decision leading to the test result
    Recognize those areas exhibiting doubtful test results that require either re-testing or assistance in interpretation and evaluation
The complexity and expense of today’s machines, equipment and tools dictate the use of fabrication and testing procedures that will ensure maximum reliability. Nondestructive testing provides many of these procedures.
The purpose of this training is to present essential knowledge of ultrasonic testing and the testing equipment relevant to ultrasonic case depth testing required by system operator personnel to enable them:

## Slide 4
Introduction
Testing Philosophy
Nondestructive testing is used to assure maximum reliability of machines, equipment and tools. To accomplish such reliability, test standards have been established and test results must meet these standards.

## Slide 5
Introduction
Personnel
It is imperative that personnel performing ultrasonic testing be trained and qualified with a technical understanding of the test equipment and materials, the part (specimen) being tested and the test procedures.
To make optimum use of ultrasonic testing, personnel conducting tests must continually keep abreast of new developments.
There is no substitute for knowledge!

## Slide 6
Introduction
Modern manufacturing procedures dictate that faulty parts be discovered as early in the manufacturing process as possible. This means that each item must be tested individually before it is required to perform in a sub-assembly, and that each sub-assembly be tested before it is required to perform in an assembly, etc.
Testing Criteria
This “building-block” approach requires that test processes be selected and test procedures be generated at the lowest level in the manufacturing process, in order that the highest level of reliability can be obtained at lowest possible cost.

## Slide 7
Introduction
Test Procedures
Approved procedures for ultrasonic testing are formulated from the analysis of test specimen, review of its history, and performance on like or similar specimens.
It is the responsibility of personnel conducting tests to ensure that test procedures are adequately applied, and that the test objective is accomplished.
Procedures found to be incorrect or inadequate must be brought to the attention of responsible supervision for correction.

## Slide 8
Introduction
Test Objective
The objective of ultrasonic testing is to ensure product reliability by providing means of:
    Obtaining a visual recorded image related to the condition in the specimen (case depth)
    Separating acceptable and unacceptable materials or parts in accordance with pre-determined criteria and standards
No test is successfully completed until an evaluation of the test results is made. Evaluation of test procedures and results requires understanding of the test objective as well as knowledge of the material being tested.

## Slide 9
Ultrasonic Principles
General
Ultrasonics is the name given to the study and application of sound waves having frequencies higher than those the human ear can detect.
Ultrasonic nondestructive testing is the use of ultrasonics to examine or test material without destroying the material. An ultrasonic test may be used to examine the internal structure of a part for possible discontinuities, such as voids or cracks, or to measure the thickness of a material, e.g. the depth (thickness) of the case.
Test frequencies commonly range from 500kHz (500,000 cycles per second) to 25MHz (25,000,000 cycles per second).

## Slide 10
Ultrasonic Principles
Sound – Energy in Motion
Sound is the mechanical vibration of particles in a medium (material). When sound waves travel in material, the particles in the material vibrate about a fixed point at the same frequency as the sound wave. The particles do not travel with the wave but only react to the energy of the wave.
It is the energy of the wave that moves through the material.

## Slide 11
Ultrasonic Principles
Modes of Vibration
If the length of a sound wave is measured from peak to peak, the distance is always the same. This distance is known as the wavelength (λ). The time it takes for the wave to travel a distance of one complete wavelength is the same amount of time it takes for the source to execute one complete vibration.
The velocity of sound (V) is calculated by the equation:
V = λ * F
Where λ is the wavelength, and F is the frequency (of the wave)

## Slide 12
Ultrasonic Principles
Modes of Vibration
Several types of sound waves travel through solid materials. There are longitudinal (compression) waves where the particles vibrate back and forth in the same direction as the motion of sound. There are also shear (transverse) waves where the particles vibrate back and forth in a direction that is perpendicular to the motion of sound.
The high frequency particle vibrations of sound waves are propagated in homogeneous solid objects in the same manner as directed light beams. Sound beams are reflected, partially or totally, at any surface acting as a boundary between the object and a gas, liquid or other type of solids. As with echo-sounding in sonar applications, the ultrasonic pulses reflect from interfaces thereby enabling detection of the presence and location of the interfaces.

## Slide 13
Ultrasonic Principles
Wave Generation
When a tuning fork is struck, it vibrates and produces sound waves by compressing the air. These waves travel through the air to the ear of the listener. The tuning fork vibrations soon die out and no longer produce waves.
Similarly, in ultrasonic testing, a short pulse of electrical current excites a transducer (crystal), which vibrates as did the tuning fork. The sound beam from the transducer then travels through a couplant (water, oil, etc.) into the test piece.

## Slide 14
Ultrasonic Principles
Wave Generation – Longitudinal Mode
← Particle Movement →
Wave Movement →

## Slide 15
Ultrasonic Principles
Piezoelectricity
To produce a sonic beam in a test piece, a transmitter applies high-frequency electrical pulses to a “piezoelectric” crystal. Piezo is derived from the Greek word meaning “to press”.
Piezoelectricity refers to a reversible phenomenon where a crystal, when vibrated, produces an electrical current; or conversely, when an electric current is applied to the crystal, the crystal vibrates.
When energized with electrical pulses, the crystal transforms the electrical energy into mechanical vibrations and transmits the vibrations through a coupling medium into the test material. These pulsed vibrations propagate through the object with a velocity that depends on the density and elasticity of the test material.

## Slide 16
Ultrasonic Principles
Soundbeam Reflection
In many ways, high-frequency vibrations act in the same way as light beams. For example, when they strike an interrupting object, most of the soundbeam energy is reflected. These reflections may then be picked up by a second, or, in most cases, by the same crystal or transducer.
Within the transducer, the mechanical energy is transformed into electrical energy, which is then sent to the test system as a vertical deflection of a horizontal trace or base line. This type of presentation is called “A-Scan” presentation.

## Slide 17
Ultrasonic Principles
A-Scan Presentation
The distance that a soundbeam travels to a reflecting surface is displayed on the screen and can be measured.

## Slide 18
Ultrasonic Principles
Soundbeam Characteristics
Common ultrasonic test instruments have frequencies available in a range from 500kHz to 25MHz. Soundbeams of all frequencies can penetrate fine-grained material without difficulty. However, when using high frequencies in coarse-grained material, interference in the form of scattering occurs.
This phenomena is used to measure case depth when high-frequency sound waves travelling through the fine-grained case, are scattered at the interface of fine-grained (case) to coarse-grained (base material).
This is referred to the “Back-Scatter” effect.

## Slide 19
Back-Scatter Effect
The ultrasonic back-scatter technique is used to nondestructively evaluate and measure the case depth (SHD) of heat-treated parts.
This technique allows the detection of the transition between different polycrystalline structures due to their variation in backscattering characteristics. Acoustic backscattering increases with the increase of the particle (grain) size because the ultrasonic dispersion coefficient is proportional to the third power of the effective particle size if the condition “wavelength larger than particle size” is true.
Ultrasonic Case Depth Measurement

## Slide 20
Ultrasonic Case Depth Measurement
Back-Scatter Effect
Induction hardening usually creates a fine-grained, near-surface structure that varies from the unhardened base material structure particularly in regard to the particle size.
While the hardened near-surface structure is very transparent to ultrasonic waves, the coarse-grained base material structure exhibits increased ultrasonic backscattering, which results in usable signal amplitudes suitable for display.

## Slide 21
Ultrasonic Case Depth Measurement
Back-Scatter Effect
Micro-Structure Case Pattern

## Slide 22
Ultrasonic Case Depth Measurement
Back-Scatter Effect
Transducer
Case
Case Depth
Base Material

## Slide 23
Ultrasonic Case Depth Measurement
Measurement Technique
Case Depth

## Slide 24
Measurement Technique
The case depth is measured by evaluating the transit time of the ultrasonic pulse when entering the material surface to the case-to-base material interface. The case depth (SHD) is computed without additional calibrations using the given sound velocity of carbon steel and the angle of incidence with the following equation:
Where:
ν = Sound velocity of carbon steel
t = Transit time from entry surface to the base material interface
ß = Angle of incidence in the case material
Ultrasonic Case Depth Measurement

## Slide 25
Ultrasonic Case Depth Measurement
Measurement Technique
A sharp hardness gradient in the transition area provides excellent ultrasonic data that agree very well with the SHD values determined by destructive methods (e.g., Vickers micro-hardness testing).
The ultrasonic back-scatter technique is applicable for case depths of 1.0mm (0.040”) and greater, and can be used to measure the case depth of simple and complex contoured parts, e.g., fillets and radii. The reproducibility of the ultrasonic case depth data is typically within +5% of the case depth.

## Slide 26
Ultrasonic Case Depth Measurement
Measurement Technique
As back-scattered ultrasonic signals have a distinct interference structure (due to the phase-sensitive measurement), it is necessary to average the received signal values for increased measurement accuracy.
More accurate results are obtained through “local averaging”, where the specimen is turned in a pre-determined angular range. During the rotation, each backscattered signal is summarized and then averaged. Alternatively, the search unit may be moved with slight forward/backward movements in the desired test location to receive a smooth averaged A-Scan. The “quiver” movement area can be as small as 1.0mm (0.040”) to achieve accurate test results.

## Slide 27
Ruggedized rack-mount PC
Intel Core™ i7-7700k, 4.20GHz CPU; 2x 8GB DDR4 3466MHz RAM
500GB & 2TB HDD and Blu-ray drive
22” monitor, keyboard and touch pad
Standard PC ports, such as HDMI, LAN RJ-45, PS-2 combo, USB 2, USB 3 and 3.1, etc.
BNT RF cable connectors (male)
Ultrasonic Test Instrument
Industrial PC
The standard PC-based test system consists of the following main components:

## Slide 28
Ultrasonic Test Instrument
Industrial PC

## Slide 29
Ultrasonic Test Instrument
Industrial PC
RF Cable Connectors, 6 Channel System

## Slide 30
Ultrasonic Test Instrument
Pulser/Receiver Board – Transmits and Receives UT Data
Ultrasonic Components

## Slide 31
Ultrasonic Test Instrument
Ultrasonic Components
Standard Ultrasonic Transducers

## Slide 32
Ultrasonic Test Instrument
Ultrasonic Components
Fitted Ultrasonic Search Unit

## Slide 33
Ultrasonic Test Instrument
Safety Information
The P31-Series test instrument was designed and built in accordance with national and international standards and specifications. The instrument complies with the requirements of the relevant CE specification, certified by the CE Compliance document (ISO-9000) and by the CE Mark.
Chapter A.3 of the User Manual provides General Safety Information in more detail.

## Slide 34
SHD Studio Testing Software
General
The ultrasonic case depth testing is completely software driven. The current version (1.11) runs under Windows 7 Professional (64-bit), SP1.
The next slides show how to operate the SHD Studio software.

## Slide 35
Basic Settings – including relevant test setup variables
Programming – databases to arrange instrument and analysis settings, including transducers, wedges, and materials
Setup – display and modification of program settings including hardware parameters and display settings
Viewer – review and deletion of saved SHD inspections
Inspection – selection of the programming database and testing of the selected features
SHD Studio Testing Software
General
The SHD Studio software consists of several individual modules for setup, testing and documentation:

## Slide 36
SHD Studio Testing Software
Basic Settings
The Basic Settings contains several parameters required by the software to acquire ultrasonic data and relevant database information, such as Optional Parameters to generate inspection reports.
In addition, this menu allows backup of the current database, and can be used to change the password for Level II and Level III users.
The settings for the Report Directory, Report Template Directory and the Screen Shot Directory can be selected in the Basic Settings menu.

## Slide 37
SHD Studio Testing Software
Basic Settings
The Measurement Unit (mm or inch), Decimals (1, 2 or 3) and the Language (German, English, Chinese, French, Spanish, Korean and Portuguese) can be selected in the Basic Settings.

## Slide 38
SHD Studio Testing Software
Basic Settings – Materials
The Materials Catalog contains the listing for different materials to be tested. The sound velocity of the material entered here is required to control the data evaluation settings.

## Slide 39
SHD Studio Testing Software
Basic Settings – Transducers
The Transducer Catalog contains the listing of available transducers, and includes the name, serial-number, type, gain-offset and comments of the transducers.

## Slide 40
SHD Studio Testing Software
Basic Settings – Wedges
The Wedge Catalog contains the listing of available transducer wedges, including name, serial-number, sound velocity, angle, delay-offset and comments. Except for the name, serial-number and comment, these settings are required by the data analysis program and should not be changed without consulting the system manufacturer.

## Slide 41
SHD Studio Testing Software
Basic Settings – Optional Parameters
Optional Parameters to be displayed in the test reports can be selected by clicking the Optional Parameters Button.

## Slide 42
SHD Studio Testing Software
Basic Settings – Database Backup
To backup the current database, the Backup Database Button is clicked, and the directory of the backup location can be selected.

## Slide 43
SHD Studio Testing Software
Basic Settings – Change Password
The password (Level II – Supervisor) can be changed by clicking the Change Password Button and entering the current and new password.

## Slide 44
SHD Studio Testing Software
Basic Settings – Level III
The Basic Settings in the Administrator (Level III) mode provides five additional settings. Manual Scan, Auto-Scan, Internal Notations, Translator and Channels.

## Slide 45
SHD Studio Testing Software
Basic Settings – Level III
The Manual Scan settings provides the selection of two A-Scan presentations:
#1: A-Scan with detailed information
#2: A-Scan without detailed information

## Slide 46
SHD Studio Testing Software
Basic Settings – Level III
The Auto-Scan settings are only available for automatic scanning with system integrated position encoders.

## Slide 47
SHD Studio Testing Software
Basic Settings – Level III
The Internal Notations Button shows the software-based Buttons for the Basic Settings, Programming, Setup, Viewer and Inspection menus.
When the Translator Button is clicked, the Translator window opens and displays the language settings for Labels, Buttons, Words and Dialogs.

## Slide 48
SHD Studio Testing Software
Basic Settings – Level III
The Channels Button permits the selection of available ultrasonic channels (1 – 8), required for the Programming of the Parameter Sets.

## Slide 49
SHD Studio Testing Software
Programming
The Programming menu is used to prepare Master Records, Features and Feature settings, such as Materials, Transducers, Wedges, Offset, etc., for the parts to be inspected.

## Slide 50
SHD Studio Testing Software
Programming – Master Records
Existing Master Records can be copied, edited or deleted.

## Slide 51
SHD Studio Testing Software
Programming – Master Records
To edit or create new Master Records the following settings can be edited or created:
Master Record: Enter the name of the part to be tested
Created by: Enter the originator name
Modified: Change the modification date
Select Optional Parameter: Choose optional parameter
Comment: Add comments
Save the edited data by clicking the Save Setup Button.

## Slide 52
SHD Studio Testing Software
Programming – Master Record, Feature
Existing Features of the selected Master Record can be rearranged, deleted or copied using the appropriate Buttons.

## Slide 53
SHD Studio Testing Software
Programming – Master Record, Feature Settings
The Feature Settings include the following information:
Name of the feature, Transducer Channel, Parameter Set, Material, Transducer, Wedge, Offset, SHD Factor, Min. Depth, Max. Depth, Shape and Comments.

## Slide 54
SHD Studio Testing Software
Setup
The Setup window is used to display and modify the settings for accurate case depth testing. The Buttons in the left side of the window provide the following functions and settings:
Start: Executing data acquisition of the selected parameter set.
Report: Go to the Report menu
Shade: Provides two colored shades for the entry signal and backscatter signal
RF Signal: Transfer from high-frequency signal to rectified signal
Expert: Switches to Expert Mode
Save: Save current settings
Load: Import existing Parameter Set
Reset: Reset current settings

## Slide 55
SHD Studio Testing Software
Setup – Start
The Setup window shows the last loaded Parameter Set. To use a different Parameter Set, the load Button must be clicked.

## Slide 56
SHD Studio Testing Software
Setup – Load Parameter Set
After the Load Button is selected, the program displays the list of available Parameter Sets. The Parameter Set is selected by clicking the desired Parameter Set and selecting the Load Button.

## Slide 57
SHD Studio Testing Software
Setup – Start
After the desired Parameter Set is loaded, the Start Button or  is clicked to start data acquisition using the selected Parameter Set on the part to be inspected.

## Slide 58
SHD Studio Testing Software
Setup – Start
The A-Scan display shows the rectified signal of the test location. The blue markers indicate the time-of-flight difference of the entry signal and the backscatter signal to determine the case depth at the current location.

## Slide 59
SHD Studio Testing Software
Setup – Start
The first marker (left) is centered at 85% height of the entry signal (surface signal), and the second marker is aligned to 25% height of the backscatter signal.

## Slide 60
SHD Studio Testing Software
Setup – Start
The Case Depth field displays the measured case depth (mm) and The Time-of-Flight field shows the time-of-flight between the two markers.

## Slide 61
SHD Studio Testing Software
Setup – Start
The Case Depth Display to the right of the A-Scan is only available when a position encoder is installed on the system.

## Slide 62
SHD Studio Testing Software
Setup – Start
Additional data such as Hardware settings, General data, Geometry shape and Case Depth Display are shown at the bottom of the window.

## Slide 63
SHD Studio Testing Software
Setup – Start
The Hardware section displays the selected settings of the Parameter Set. Delay determines the distance of the transducer entry signal (µsec). Sample Length is the horizontal space of the A-Scan display (µsec) Gain identifies the amplitude height of the receiver signals. Average arranges the number of averaged signal (digits). Transmitter Channel is the selected transmitter and Receiver Channel is the selected receiver.

## Slide 64
SHD Studio Testing Software
Setup – Start
The General section displays the selected settings of the Parameter Set. Smoothing determines the length of the half-cosign signal smoothing filter. Material shows the material from the Material Catalog. Wedge displays current wedge from the Wedge Catalog. Transducer exhibits the transducer from the Transducer Catalog.

## Slide 65
SHD Studio Testing Software
Setup – Start
The Shape allows the selection of Unknown, Rectangle or Circle. Unknown shows no Geometry. Rectangle displays the case depth location in rectangular format. Circle presents the cased depth location in circular format. The Offset shows Yes or No if an offset value is selected.

## Slide 66
SHD Studio Testing Software
Setup – Start
The Case Depth Display options are only available when position encoders are installed on the SHD system.

## Slide 67
SHD Studio Testing Software
Setup – Report Management
The A-Scan button saves the A-Scan image to a selectable directory. A-Scan & Shades saves the A-Scan image with entry signal shades to a selectable directory. A-Scan (.csv) saves the A-Scan image as a csv file. Screen Shot saves the current window image to the directory selected in the Basic Settings. Report Template, selection of available print templates. L&L Designer is used to edit an existing Report Template or to create a new Report Template.

## Slide 68
SHD Studio Testing Software
Setup – Shade
The Shade button provides two colored shade for the entry signal and backscatter signal in the A-Scan display.

## Slide 69
SHD Studio Testing Software
Setup – RF Signal
The RF Signal button changes high-frequency signals to rectified signals.

## Slide 70
SHD Studio Testing Software
Setup – Expert Mode
The settings for the selected Parameter Set can be adjusted in the Expert Mode using the Expert button. When the Start button is selected, the Expert Mode shows all changes made as described in the next slides.

## Slide 71
SHD Studio Testing Software
Setup – Expert Mode
The Surface Signal section displays the settings of the selected Parameter Set and permits to change the following values: Search Start determines the start position of the surface signal (µsec); Search Width determines the length of the surface signal (µsec); Amp. Decrease defines the height difference from top of the surface signal; Min. Amp. is the minimum amplitude height (%); Echo Fix adjusts the surface signal marker; Fixed Signal is a static time value (µsec) for the surface signal marker.

## Slide 72
SHD Studio Testing Software
Setup – Expert Mode
The Backscatter Signal segment shows the settings of the selected Parameter Set of the Backscatter Signal and permits to change the following values: Search Start determines the start position of the backscatter signal (µsec); Search End defines the end position of the backscatter signal (µsec); SHD Marker states the height of the marker position of the backscatter signal; Min. Amp. is the height difference from top of the surface.

## Slide 73
SHD Studio Testing Software
Setup – Expert Mode
The e-Function displays the current system settings: Length determines the range of maximum backscatter signal comparison; Increase determines the e-Function increase value; Correlation defines the acceptable signal strength of the maximum backscatter signal.

## Slide 74
SHD Studio Testing Software
Setup – Expert Mode
The Analysis sector displays the current system settings: Offset allows changes to the case depth readings by adding or subtracting offset values; SHD Factor is a multiplier for case depth readings adjustment.

## Slide 75
SHD Studio Testing Software
Setup – Expert Mode
The General section displays the current settings: Smoothing determines the length of the half-cosign smoothing filter; Material shows the material from the Material Catalog; Wedge shows the wedge from the Wedge Catalog; Transducer shows the transducer from the Transducer Catalog. All settings, except the Angle and Sound Velocity, can be changed.

## Slide 76
SHD Studio Testing Software
Setup – Expert Mode
The Hardware displays the current settings: Delay determines the distance of the transducer entry signal (µsec); Voltage is the hardware voltage settings; Sample Length is the horizontal distance of the A-Scan display (µsec); Filter shows the frequency filter (MHz); Gain identifies the amplitude height of the receiver; Dead Time is the length of the test cycle; Average is the number of averaged signals (digits); Sample Rate is the number of samples (MS/Sec); Transmitter Channel is the selected transmitter and Receiver Channel is the selected receiver.

## Slide 77
SHD Studio Testing Software
Setup – Expert Mode
The Position Encoder shows the current settings: Resolution 1 determines the input resolution of encoder 1; Resolution 2 determines the input resolution of encoder 2; Unit 1 and Unit 2 is the value in mm/inch or degree (°); Auto Reset 1 and Auto Reset 2 provides the option for Off or On for the Position Encoders. As mentioned previously, the Position Encoder options are only available when position encoders are installed on the SHD system.

## Slide 78
SHD Studio Testing Software
Setup – Expert Mode
The information at the right of the A-Scan display show the current A-Scan results. When the Amp. Surface Echo, Amp. Backscatter Echo and Correlation e-Function sections are green, the case depth readings are acceptable. If any evaluation result is red, the test results are out of the acceptable range. The window also displays the Case Depth, Time-of-Flight and Correlation information.

## Slide 79
SHD Studio Testing Software
Inspection
When the Inspection button is clicked, the Inspection window opens as shown below.

## Slide 80
SHD Studio Testing Software
Inspection
To start a new inspection, a relevant Master Record must be selected by using the New button. After the New button is clicked, the New Measurement window opens and shows available Master Records. The desired Master Record is selected with the mouse cursor and by clicking the OK button.

## Slide 81
SHD Studio Testing Software
Inspection
When the OK button is clicked, the screen displays the test information for the first feature as shown below.

## Slide 82
SHD Studio Testing Software
Inspection
To acquire the case depth data of the selected location, the search unit is placed on the part and the Start button or  key is clicked and the case depth data will be collected.

## Slide 83
SHD Studio Testing Software
Inspection
The test results from the Main Journal – Left with a case depth of 3.84mm are displayed. The data acquisition will be stopped by clicking the Stop button or  key.

## Slide 84
SHD Studio Testing Software
Inspection
To continue to the next Feature, click the Save & Continue button or  key.

## Slide 85
SHD Studio Testing Software
Inspection
After the data for all features have been acquired, click the Complete Test button or  key to save the test data.

## Slide 86
SHD Studio Testing Software
Inspection
After the data for all features have been saved, Optional Parameters (as determined in the Master Record Settings) can be selected. The Optional Parameter window permits the selection of Operator, Master Record, Inspection Comments, Feature Comment and Part ID.

## Slide 87
SHD Studio Testing Software
Viewer
The Viewer window shows all saved inspection data and can be used to print test Reports, show Optional Parameter, Filter Viewer of measurements, Delete records, inspection Comments and Analysis.

## Slide 88
SHD Studio Testing Software
Viewer - Report
When the Report button is clicked, the Report Management window shows the following options. A-Scan, A-Scan & Shades, A-Scan (.csv), Screen Shot, Print to PDF, Print to Printer, Report Template, L&L Designer and Cancel.

## Slide 89
SHD Studio Testing Software
Viewer – Optional Parameters
The Optional Parameters window shows the selected optional parameters of the current Master Record.

## Slide 90
SHD Studio Testing Software
Viewer – Filter Viewer
The Filter viewer permits the user to select Master Record, Start Date, End Date, Measurement Completed, Accepted Measurements and Rejected Measurements. When any of the filters are selected, clicking the Accept button shows the selected Measurements.

## Slide 91
SHD Studio Testing Software
Viewer – Delete
The current (highlighted) Measurement can be deleted by clicking the Delete button. After the Delete button is clicked, the deletion must be confirmed by clicking the Yes button.

## Slide 92
SHD Studio Testing Software
Viewer – Analysis
When the Analysis button is clicked, the Analysis Dialog window opens.

## Slide 93
SHD Studio Testing Software
Viewer – Analysis
Selecting the Set Cursor button allows the user to move the red curser of the backscatter signal in a different horizontal location.

## Slide 94
SHD Studio Testing Software
Viewer – Analysis
The curser of the backscatter signal has been moved to 40% amplitude height and now shows a case depth of 4.96mm. To accept the current settings, the Accept button must be clicked.

## Slide 95
SHD Studio Testing Software
Viewer – Analysis
When the Accept button is clicked, the change must be confirmed by clicking the Yes button, or declined by clicking the No button.

## Slide 96
SHD Studio Testing Software
Viewer – Analysis
After the Accept button is clicked, the changed A-Scan and Case Depth reading is displayed in the Viewer window.

## Slide 97
SHD Studio Testing Software
Viewer – Analysis
When the Change Param. button is selected, the parameters for the Surface Signal, Backscatter Signal, e-Function and Smoothing can be changed. Any changes will be saved when the Apply button is clicked.

## Slide 98
SHD Studio Testing Software
Viewer – Report Management
When the A-Scan button is clicked, the currently selected measurement can be saved as a jpg file as shown below.

## Slide 99
SHD Studio Testing Software
Viewer – Report Management
When the A-Scan & Shades button is clicked, the currently selected measurement can be saved as a jpg file as shown below.

## Slide 100
SHD Studio Testing Software
Viewer – Report Management
When the A-Scan (.csv) button is clicked, the currently selected measurement will be saved as a csv (comma separated value) file.

## Slide 101
SHD Studio Testing Software
Viewer – Report Management
When the Screen Shot button is clicked, the current measurement screen will be saved as a jpg file in the selected Screen Shot Directory, including the current date and time.

## Slide 102
SHD Studio Testing Software
Viewer – Report Management
When the Print to PDF button is clicked, the Test Report of the current inspection will be saved as a pdf file in the specified Report directory, including the current date and time.

## Slide 103
SHD Studio Testing Software
Viewer – Report Management
When the Print to Printer button is clicked, the Test Report of the current inspection will be printed to the connected printer.

## Slide 104
SHD Studio Testing Software
Viewer – Report Management
Selecting the Report Template button enables the selection of a different Template as specified in the Basic Settings.

## Slide 105
SHD Studio Testing Software
Viewer – Report Management
The L&L Designer button permits editing an existing Report Template or to create a new Report Template.

## Slide 106
Test Preparations
Test Equipment
The PC-based P31-Series case depth testing system is primarily a test instrument. The system incorporates an advanced ultrasonic data acquisition and analysis software package built on the convenience of the Windows 7 (64-bit) platform. The system’s functionality has been thoroughly tested in the configuration in which it was delivered.
Any software/hardware alterations and/or additions may corrupt the test system configuration. It is strongly suggested to backup the entire system prior to installing any additional software and/or hardware.

## Slide 107
Correct operation of the test instrument
Efficient usage of the testing system
Accurate test results
Avoidance of system breakdown and production outage
Prevention of injuries during system operation
Test Preparations
Test Equipment
It is strongly recommended that the entire User Manual be read prior to using the test instrument. The User Manual should always be readily accessible and available for reference.
The instructions and information contained in the User Manual help to assure:

## Slide 108
Test Preparations
Test Equipment
Prior to power-up of the test system, it is recommended that all cables, e.g. power cables, monitor cables, RF cables (at the PC and at the search unit), etc., be checked for proper connection.
After power-up of the computer system and user logon, sufficient time should be allowed for the system to perform internal boot-sequences and stabilization.
When the hard disk indicator light stops blinking the system is ready to launch the SHD program.
To avoid short-circuit damage to the pulser/receiver board, never connect or disconnect RF cables from the transducer or the system during data-acquisition; always stop data-collection before changing transducers or cables!

## Slide 109
Test Preparations
Test Specimen
The test specimen should be clean and free of paint or loose scale in the inspection areas. Light corrosion should not have any negative impact. However, heavy rust or excessive tool marks may lead to difficulties during data acquisition and analysis.
Finished (polished) test surfaces may also lead to undesirable poor sound transmission due to lack of couplant on the test surface.

## Slide 110
Data Protection, System Backup
To assure that installed programs, system settings, database entries and saved test data are not lost, it is recommended that the entire system (C-drive) is backed up at regular intervals using the pre-installed backup program (Acronis).
It is strongly suggested that the C-drive is backed up prior to installing any third-party software programs to avoid accidental loss or replacement of executable and or setup files vital for the test software.
For more information on setup and running the Acronis backup software, consult the Acronis User guide documentation.
Documentation

## Slide 111
Summary
Ultrasonic testing to determine the case depth of ball-path, tooth-gear, or other areas can be performed by utilizing the P31-series case depth testing system with appropriately designed search units.
Following the instructions provided during this training and in the User Manual, enables system operators to generate meaningful and reliable data to assess the case depth quality of the parts.
The next few slides summarize the recommended 10-Step procedure to acquire and document case depth data.

## Slide 112
Ten Steps to Acquire Case Depth Data
Power-up the test instrument and logon to Windows 7
Select the proper search unit and connect the RF cables to the instrument (search unit connectors)
Run the SHD-Studio program from the Start menu or the shortcut on the desktop
When the SHD-Studio program is open, click the Inspection button (top left) and click the New button.
To start the inspection, select the desired Master Record and click OK to start the Measurement.
Summary

## Slide 113
Ten Steps to Acquire Case Depth Data
Place a sufficient amount of couplant onto the test surface and position the search unit on the sample
Click the Start button (or ) and slightly quiver the search unit in the inspection area to obtain a stable A-Scan image and depth reading
Press the Stop button (or ) and proceed to the next feature by clicking the Save & Continue button
After the data are collected for all features, click the Complete Test button to save the inspection data
To end the inspection, the Close button is clicked
To avoid short-circuit damage to the pulser/receiver board, never connect or disconnect RF cables from the transducer or the system during data-acquisition. Always stop data-collection before changing transducers or cables!
Summary

## Slide 114
License Agreement
Grant of License
Quality Network Inc. (QNET) grants you the nonexclusive and nontransferable right during the term of this agreement to use this material only for your own benefit and the benefit of your organization.
This means that the following may use this material: (I) your company (at any site owned and operated by your company); (II) its subsidiaries or other related entities; and (III) a consultant to your company or related entities, if the consultant has entered into a contract agreeing not to disclose the material outside of its organization or to use the material for its own benefit or the benefit of any party other than your company.

## Slide 115
License Agreement
Copyright
This material, including the information contained in it, is owned by QNET and is protected by United States and international copyright laws.
You may not, without the prior written permission of QNET, reproduce, translate, or modify this material, in any form, in whole or in part, or prepare any derivative work based on this material.

## Slide 116
License Agreement
Restrictions
You may not rent, lease, license, disclose or give this material to any person or organization, or use the information contained in this material, for the benefit of any third party or for any purpose other than as specified above unless such use is with the prior written permission of QNET.
You agree to take all reasonable steps to prevent unauthorized disclosure or use of this material.
Except as specified above, this agreement does not grant you any right to patents, copyrights, trade secrets, trade names, trademarks or any other intellectual property, rights or licenses in respect of this material.

## Slide 117
License Agreement
Term and Termination
This license and this agreement are effective until terminated. You may terminate them at any time by destroying this material.
QNET has the right to terminate the license and this agreement immediately if you fail to comply with any term or condition of this agreement.
Upon any termination you may destroy this material, but all obligations of nondisclosure will remain in effect.

## Slide 118
License Agreement
Disclaimer of Warranties and Limitation of Liabilities
Neither QNET, any member of QNET, any co-sponsor, nor any person or organization acting on behalf of any of them:
(A) Makes any warranty or representation whatsoever, express or implied, (I) with respect to the use of any information, apparatus, method, process or similar item disclosed in this material, including merchantability and fitness for a particular purpose, or (II) that such use does not infringe on or interfere with privately owned rights, including any party’s intellectual property, or (III) that this material is suitable to any particulars user’s circumstance, or
(B) Assumes responsibility for any damages or other liability whatsoever (including any consequential damages, even if QNET or any QNET representative has been advised of the possibility of such damages) resulting from your selection or use of this material or any information, apparatus, method, process or similar item disclosed on this material.

## Slide 119
License Agreement
Integration
You have read and understand this agreement, and acknowledge that it is the final, complete and exclusive agreement between you and QNET, concerning its subject matter, superseding any prior related understanding or agreement.
No waiver, variation or different terms of this agreement will be enforceable against QNET unless QNET gives its prior written consent, signed by an officer of QNET.